# 30
## Brief
Rename file using FCB
## Input
DS:DX → modified FCB (see also FCB) the old filename ('?' wildcards OK) is in the standard location while the new filename ('?' wildcards OK, no drive) is stored in the 11 bytes beginning at offset 11h
## Return
- AL = status
  - 00h successfully renamed
  - FFh no matching files,file is read-only, or new name already exists
## Notes
subdirectories may be renamed using an extended FCB with the appropriate attribute, as may volume labels
## See also